## Slide 1
CSO / OPERATIONS / PMO
Cleaning of bulk vessels
Improve safety and operational efficiency while reducing vessel turnaround time.
OPERATIONAL IMPROVEMENT PROPOSAL · OCTOBER 2026

## Slide 2
CSO / OPERATIONS / PMO
Current state
Where cleaning sits in the operation today.
BREAKBULK
Vessel · Quay · Yard
Dunnage, strapping and waste are generated during cargo handling.
Residual material in holds, on the quay or in the yard requires further cleaning.
Loose debris creates lifting, vehicle and housekeeping hazards.
Cleaning is not always fully integrated into cargo handling, creating additional work.
DRY BULK
Cargo hold
Loader / excavator normally enters when ~20% of cargo remains.
Cargo may be compacted along hold sides and between vessel frames.
Late recovery is time-consuming and can require extra equipment (cherrypicker).
Extended final cleaning can delay completion of discharge and vessel departure.
OPERATIONAL IMPROVEMENT PROPOSAL · CLEANING OF BULK VESSELS
2 / 4

## Slide 3
CSO / OPERATIONS / PMO
Future state
Progressive cleaning, earlier intervention and clearly controlled working zones.
BREAKBULK
Clean as we go
Collect and segregate dunnage / waste progressively during discharge.
Use approved frames for long dunnage and suitable containers for small pieces.
Remove strapping and debris before cargo transfers and yard transport.
Proposed target: max. 15 minutes of hold cleaning after the last cargo lift.
DRY BULK
Earlier controlled recovery
Consider earlier loader / excavator deployment, subject to safety approval.
Progressively clear hold sides and frames to support discharge in even layers.
Identify safe spots, grab exclusion zones and an operating coordinator.
Simultaneous operations (SIMOPS) only with proven safe separation; otherwise perform work sequentially.
~30% discharged is a planning guideline, not automatic deployment approval.
OPERATIONAL IMPROVEMENT PROPOSAL · CLEANING OF BULK VESSELS
3 / 4

## Slide 4
CSO / OPERATIONS / PMO
Steps to implement
A coordinated improvement programme with separate approvals for each work instruction.
01
FINALISE
Finalise both work instructions with Operations and HSSE.
02
ASSESS RISKS
Conduct task-, cargo- and vessel-specific risk assessments.
03
DEFINE CONTROLS
Define OPS / HSSE roles, safe zones, radio protocol, equipment controls and SIMOPS stop rules.
04
BRIEF & TRIAL
Brief crews; apply breakbulk controls and run a supervised dry-bulk trial.
05
MEASURE & APPROVE
Compare cleaning time, safety observations, equipment use and discharge delays. Approve the method only after safety and performance evaluation.
OPERATIONAL IMPROVEMENT PROPOSAL · CLEANING OF BULK VESSELS
4 / 4